## Slide 1
Things
Cloud Gateway
(IoT Hub)
IoT Device
(MX Chip AZ3166)
Insights
Actions
Action
(Azure Function)
Stream Processing
(Azure Stream analytics)
Cold storage
(Data Lake Store gen1)
Business Integration
Analytics
(Data Lake Analytics)
1
2
3
4
5
6
7

## Slide 2
why the subsystem was chosen?
Based on provided requirements: | Implementation comments (subsystem)
The weather station will send telemetry data to the cloud (simulated using an MXChip AZ3166 Devkit). | Weather station is securely connected to cloud gateway (Azure IoT hub). Step “1” on architecture diagram.
 | Step “2”, Azure Stream analytics receives all telemetry data.
 | Step “3” Azure Stream analytics extracts "deviceId” and "windSpeed“ from telemetry data and sends extracted data to Azure function.
Data should be monitored in real-time to ensure the wind speed does not exceed safe limits. Alert condition will be indicated through the illumination of a LED (Green - Wind Speed is Normal, Orange - Wind Speed is Strong, Red - Wind Speed is Dangerous) and the increase in frequency of the transmission of telemetry data. | Step “4” Azure function: Evaluate the windspeed and update (action) device twin properties.
Data should be stored for long-term analysis. Weather station will provide telemetry data in JSON format: Temperature, Humidity, Wind Speed, Wind Direction | Step “5” Telemetry will be stored in the cloud for long-term use with Data Lake Analytics.
 | Step “6”
Azure Streaming Analytics will be used to process incoming data and direct it to the appropriate output. | Step “7”